## Slide 1: BlueROV Electronics and Controls Documentation
Original presentation: https://www.bluerobotics.com/wp-content/uploads/2016/03/BlueROV-Block-Diagram-20160318.pptx
Original forum post: https://www.bluerobotics.com/forums/topic/bluerov-interconnect-diagram/
The AUV Laboratory at MIT Sea Grant
June 24, 2016

## Slide 2
3DR Pixhawk
Autopilot
Raspberry Pi Camera Board
Ctrl / Data
Ethernet Tether
6600 mAh 4s Lipo Battery
14.8vdc
3DR Power Module
Terminal Board
XT90
XT90
XT60
XT60
GPS
BlueROV Electrical Interconnect Block Diagram
Terminal Board
+14.8V DC
Basic 30A ESC
T200 Thruster
ESCs ……6x…..
Basic 30A ESC
T200 Thruster
Thrusters ……6x…..
Pressure Enclosure
Topside (Laptop)
JST-XH
JST-XH
JST-XH
Main
Outputs
……6x….
Main ESC PWM
Thruster Ctrl
BatPwr In
Power
5V DC
Buzzer
Buzzer
(Optional)
+14.8V
Gnd
20160624
XT60
XT60
+14.8V
I2C
I2C Expander
BlueRoboticsPressure / Temp. Sensor
TELEM 2
GPIO15, 14, GND
Raspberry Pi 3
UBEC
Input 14.8V
Output 5V
5V/GND Pins
Xbox Controller

## Slide 3: Controls Interface
QGroundControl
Video Feed
Parameters and Position updates
Sensor Data
Xbox Controller
Manual Control
ArduSub
ESCs
Pi Cam
Raspberry Pi 3
Laptop
Telem2
Sensors
3DR Pixhawk
Autopilot
This is the controls interface for the final ROV setup.
Ethernet
Tether
On-Board
Topside

## Slide 4: Controls Interface- Testing
QGroundControl
Video Feed
Parameters and Position updates
Sensor Data
Xbox Controller
Manual Control
ArduSub
ESCs
Pi Cam
Raspberry Pi 3
Telem2
Sensors
3DR Pixhawk
Autopilot
This is the setup used while testing different components and software packages. Different arrangements could be more compact, but this is what was available and fastest to set up without Ethernet at the time.
Both Mac and PC were used for testing, but unless otherwise noted the interface remained the same between both platforms. An Ubuntu virtual machine on VMware was used for the PC. PuTTY saves time on the PC for SSH without booting the virtual machine.
Ubuntu VM (PC)
Laptop (PC or Mac)
Video Feed (Mac)
SSH (VM)
SSH (Mac or PC)

## Slide 5: Software Summary List of all sites consulted for software downloads, some of the links may be redundant.
https://www.bluerobotics.com/forums/topic/radio-calibration/
http://ardusub.com/initial-setup/#install-qgroundcontrol
https://github.com/mavlink/qgroundcontrol/releases/tag/v2.9.7b
http://firmware.ardusub.com/Sub/latest/
https://www.bluerobotics.com/forums/topic/bluerov-ros-package-updates/
https://www.bluerobotics.com/forums/topic/problem-with-running-bluerov/
http://www.ros.org/install/
Common error fixes
RC3_MAX and RC3_MIN change to 2200 and 800 – fixes joystick/radio calibrating
Change baud rate and a few other parameters listed here http://ardusub.com/initial-setup/#configuring-parameters
ssh into bluerov raspi when simplerov frame is installed on Pixhawk, and UDP com port on qgroundcontrol is 14550: sudo -s mavproxy.py --master=/dev/ttyAMA0 --baudrate 57600 --out LAPTOP_IP_ADDRESS:14550 --aircraft simplerov
If connection times out and mavproxy.py still running: sudo –s pkill mavproxy.py

## Slide 6
http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Pixhawk Overview
Connect ESCs Control 1-6 Here
Buzzer (Optional)
Connect I2C Expander
Then connect Pressure Sensor and BlueRobotics Depth Sensor to Expander
Connect 3DR Power Module Pigtail Here
Pi Data connects to Pixhawk via Telem 2

## Slide 7
Pixhawk connector assignments
Thruster ESCs - PWM
Pwr Input (from module)
Warning Buzzer (optional)
http://copter.ardupilot.com/wiki/common-pixhawk-overview/
Connect I2c Expander which is connected to Pressure sensor and Bluerobotics depth/temp. sensor
Comms (to Rasp. Pi3)

## Slide 8: Raspberry Pi Connectors The pins are labeled in a confusing manner, so this page is to clarify the connections necessary to run the Pixhawk and Raspberry Pi together.
http://tr1.cbsistatic.com/hub/i/2016/03/03/53945d8c-6ec9-4a2a-922a-6df3b2a5c372/img4085.jpg, http://ardupilot.org/dev/_images/RaspberryPi_Pixhawk_wiring1.jpg
UBEC 5V
UBEC GND
Telem2 #3
Telem2 #2
Telem2 #6

## Slide 9: 3DR Power Module This page explains how to set up the 3DR Power Module (PM) to measure battery voltage and current consumption. The information will also be useful for setting up other types of Power Module.
http://copter.ardupilot.com/wiki/common-3dr-power-module/
XT60 Connector
To BlueROV
Terminal Board +/Gnd
To Pixhawk Power Input Conn.
3DR Power Module
3DR Power Module-
Reverse Side
+5vdc
Gnd

## Slide 10: UBEC This page explains how to set up the 3A-6s UBEC Voltage regulator to power Raspberry Pi from LiPo safely.
http://www.brontoseno.com/kategori-produk/sbecubec/
To BlueROV
Terminal Board +/-
Turnigy UBEC-5A
Input
To Raspberry Pi 5V and Gnd pins
Output

## Slide 11: ESC Connections
http://docs.bluerobotics.com/assets/images/documentation/besc-labels.png
5V not needed, cut the connections to avoid overheating
Motor directions determined by output phase, exact wiring not known until tested

## Slide 12
Comments:
The “safety sw” is currently disabled in our recommended
Changes have been made to diagram to power Raspberry Pi separately from Pixhawk
ESC 5V connections removed by rec.
GPS/Compass removed because ocean water
Slides 1, 3, 4, 5, 8, 10, 11 added for clarity

## Slide 13: Additional Sources
https://www.bluerobotics.com/wp-content/uploads/2016/06/Diagram-Mockup-Ethernet.jpg
https://www.bluerobotics.com/forums/
http://ardupilot.org/dev/docs/raspberry-pi-via-mavlink.html
http://ardusub.com/initial-setup/#configuring-parameters
https://www.bluerobotics.com/forums/topic/radio-calibration/

## Slide 14: Additional Images

## Slide 15: Additional Images